| Ref: 235/2015 | Description: Operation of an electrically powered CNC milling machine |
| --- | --- |
| Assessment Date: 2nd December 2015 | Location/Site: DL Main Workshop, ETC Building, Daresbury |
| Assessor: John Smith | Department: Technology |
| Assessment Team: David Adams (operator) Ryan Jones (Line Manager), John Smith (engineer) | Persons Exposed: Milling Machine Operator, STFC Staff , Visitors |
| Activity/Task: Transport of metal stock from store to the milling machine Mounting metal stock in the milling machine Operating the milling machine Removal of finished work Disposal of waste The building is covered by a separate fire risk assessment which is held in the SHE database. |
| Step 1 What are the hazards? | Step 2 Who might be harmed and how? | What are you already doing? (see guidance attached) | What is the level of risk? (see guidance attached) | Step 3: What further action is necessary? | Step 4: How will you put the Assessment into action? |
| Hazard/Task or Situation |  |  | H Harm | L Likelihood | R Risk |  | Action by whom | By when | Done |
| Electricity The milling machine is electrically operated. | Machine Operator: Electric shock from exposed or damaged wiring. | Engineering Controls: The machine is permanently wired-in and all electrical connections are fully insulated. Administrative Controls: Electrical work on the machine is subject to SC34 and may only be performed by suitably trained and authorised staff. See SC34 | Moderate | Very Unlikely | Low | Machine operator to visually check the external electrical wiring and connections for signs of damage before use. | Joe Bloggs | 15/01/2016 |  |
| Manual Handling Moving metal stock to and from the milling machine | Machine Operator: Musculoskeletal injury from use of incorrect or inappropriate lifting techniques. | Eliminate/Substitute: All staff are advised not to undertake any unnecessary manual handling. The workshop supervisor should be contacted if special handling requirements are necessary, Engineering Controls: Small trolleys are available for moving items over long distances. Administrative Controls: All staff are trained in Manual Handling. See SC12 | Moderate | Likely | Medium | Emphasise to staff the importance of following guidance and keeping manual handling training up to date | Joe Bloggs | 26/02/2016 |  |
| Contact with moving machinery The milling machine contains sharp, high-speed moving parts. | Machine Operator: Severe cuts or loss of finger(s) from contact with moving machine parts and tools. | Engineering Controls: The milling machine is fitted with several guards designed to prevent access to moving parts. Most of the guards are interlocked but one is removable to allow limited essential access to the part being machined. Administrative Controls: Only trained workshop staff are permitted to operate the machine. PPE: Overalls should be worn when operating the machine. Gloves are available if necessary. | Moderate | Unlikely | Medium | None |  |  |  |
| Chemicals Use of cleaning fluids and lubricants. | Machine Operator: Skin or eye irritation from contact with cleaning fluids or machine lubricants. | Eliminate/Substitute: Quantities used should be kept to a minimum. Engineering Controls: Chemicals are kept in a dedicated storage area when not in use. Administrative Controls: A COSHH assessment has been completed and Safety Data Sheets are available. Use of chemicals by trained staff only. Use is restricted/controlled. PPE: Overalls, gloves and safety glasses are available. See SC37 | Slight | Unlikely | Low | None |  |  |  |
| Noise Operation of the milling machine and other machines in the workshop | Machine Operator, STFC Staff, Visitors: Temporary or permanent hearing damage as a result of exposure to excessive noise levels. | Engineering Controls: Most machines in the workshop have some form of cover which helps to reduce overall noise levels. Administrative Controls: A noise survey has been undertaken. Levels are generally below action levels. PPE: Ear plugs are available from the office for operators, staff and visitors if required. See SC18 | Moderate | Very Unlikely | Low | None |  |  |  |
| Sharp objects Machine tools and swarf. | Machine Operator, STFC Staff, Visitors: Cuts and contusions from sharp machine tools and swarf left in accessible areas. | Eliminate/Substitute: Workplace should be kept tidy. Tools stored in dedicated storage areas and swarf put in a dedicated skip for disposal. Administrative Controls: Staff trained to recognise the hazards in a workshop environment. Visitors to be accompanied by a trained member of staff at all times. PPE: Overalls, gloves and safety glasses available for machine operators. | Slight | Likely | Low | The skip used for disposal of swarf was full and located adjacent to the walkway used by STFC Staff and visitors increasing the likelihood of inadvertent contact. Re-siting the skip away from the walkway would be advantageous. | Joe Bloggs | 15/01/2016 |  |
| Lone Working | Machine Operator: Injury or death resulting from lack of assistance. | Eliminate/Substitute: Lone working not permitted under normal circumstances. Engineering Controls: When undertaking authorised lone working the security-monitored lone worker system should be used. Administrative Controls: A “buddy” system will be used when authorised lone working is required, | Slight | Unlikely | Low | None |  |  |  |
| General Workshop Environment | Machine Operator, STFC Staff, Visitors: Slips, trips and falls as a result of trailing cables, liquid spills, inappropriately placed equipment etc. | Eliminate/Substitute: Ensure good housekeeping. Administrative Controls: STFC Staff should make themselves aware of the potential hazards before entering the workshop. Visitors to be escorted at all times. | Slight | Unlikely | Low | None |  |  |  |
| Distribution List: | Signed: | Date: |
| Brian Martlew |  |  |
| Workshop Manager |  |  |
| SHE representative |  |  |
| Step 5 Review Date: 2nd December 2016 | Review your assessment to make sure you are still improving, or at least not sliding back. If there is a significant change in your workplace, remember to check your risk assessment and where necessary, amend it. |

What is the level of risk? For each hazard, choose determine the Harm and Likelihood. Look for ‘the most likely reasonably foreseeable injury’ not just the worst case.

| H - Harm - Decide How Someone Might be Harmed |
| --- |
| Major | Fatality. |
| High | Amputations; multiple serious injuries; major fractures; major burns. |
| Moderate | Lacerations; burns; concussion; serious sprains; minor fractures. |
| Slight | Superficial injuries; minor cuts and bruises; eye irritation from dust. |
| L - Likelihood - How Likely is it to Happen? |
| Very Unlikely | The hazard is very rarely experienced and exposure will seldom result in injury. |
| Unlikely | The hazard is rarely experienced and exposure will seldom result in injury. |
| Likely | The hazard is persistent but exposure may not always result in injury. |
| Very Likely | The hazard is persistent and exposure will undoubtedly result in injury. |

Now use the matrix below to assess the Risk from the Harm and Likelihood for each hazard

(e.g. if Harm was ‘Moderate’ and Likelihood ‘Unlikely’ the Risk would be ‘Medium’).

Risk table – to calculate the risk of each hazard use the table below:

| Harm | Major | High | High | V High | V High |
| --- | --- | --- | --- | --- | --- |
|  | High | Med | Med | High | V High |
|  | Moderate | Low | Med | Med | Med |
|  | Slight | Low | Low | Low | Low |
|  |  | Very Unlikely | Unlikely | Likely | Very Likely |
|  |  | Likelihood |

Where

| Low Risk | No additional controls are necessary unless they can be implemented at very low cost (in terms of time, money and effort). Actions to further reduce these risks can be assigned low priority. |
| --- | --- |
| Medium Risk | Consideration should be given as to whether the risks can be lowered, where applicable, to a low risk level, but the costs of additional risk reduction measures should be take into account. The risk reduction measures should be implemented within a defined time period. |
| High Risk | Substantial efforts should be made to reduce the risk. Risk reduction measures should be implemented urgently within a defined time period and it might be necessary to consider suspending or restricting the activity, or to apply interim control measures, until this has been completed. Considerable resources might have to be allocated to additional control measures. |
| Very High Risk | These risks are unacceptable. Substantial improvements in risk controls are necessary. The work activity should be halted until risk controls are implemented. If it is not possible to reduce risk the work should remain prohibited. |

What are you already doing? The ‘Control Hierarchy’ provides a simple prompt to consider the various types of control measure that are or could be established for any given hazard. The examples below are provided for illustration but are not an exhaustive list.

| Eliminate/Substitute | Redesign job or substitute a substance so hazards are removed or eliminated. For example, avoid working at height or substitute a carcinogenic substance with a less hazardous substance. |
| --- | --- |
| Engineering Controls | For example: Local Exhaust Ventilation (LEV) to control risks from dusts or fumes; Interlocks/guarding of machinery; Access control; Emergency stop within reach. Also, the complete enclosure of the operator or the hazardous machinery/equipment. Give priority to measures which protect collectively over individual measures. |
| Administrative Controls | For example: training; reducing the time workers are exposed to hazards (e.g. by job rotation); prohibiting lone working; prohibiting use of mobile phones in hazardous areas; safety signage. Also, performing risk assessments, safe systems of work or a laser standing order. |
| Personal Protective Equipment (PPE) | Only used as a control measure after all the previous measures have been considered and determined to be ineffective in controlling the risks to a reasonably practicable level. For example: safety shoes, gloves, safety spectacles, hard hat, fall arrest harnesses. It is not sufficient to say ‘PPE used’, the type of PPE required must be detailed. |

Note: if one section such as PPE is not applicable, do not delete it but instead insert “PPE: N/A”.  This shows that it has been considered and deemed not relevant for this activity.